## Slide 1: Service Line Detection
of busses using Hidden Markov Models
Sven Milker

## Slide 2: Agenda
Introduction
Hidden Markov Models
Viterbi
Modeling
Implementation
Evaluation
Conclusion
Future Works

## Slide 3: Introduction
What does „Service Line Detection“ mean?

## Slide 7: Introduction
What does „Service Line Detection“ mean?
What did others do?
What is our approach?
Predicting Bus Arrival Time (Zhou, Zheng & Li, 2014)
Transportation Mode Detection
  Shah, Wan, Lu & Nachman (2014)
  Stenneth, Wolfson, Yu & Xu (2011)
Live+Gov

## Slide 8: Hidden Markov Models
Stochastical Model
Elements
  States
Rabiner (1989)

## Slide 9: Hidden Markov Models

## Slide 10: Hidden Markov Models
Stochastical Model
Elements
  States
  Observations

## Slide 12: Hidden Markov Models
Stochastical Model
Several Elements
  States
  Observations
Probabilites
  State transition probability:
  Observation probability:
  Initial state probability: πi

## Slide 14: What can we do with it?
Compute probability of an observation sequence
Compute corresponding state sequence

## Slide 15: Viterbi
Clever way to compute state sequence
Uses intermediate data
Recursively computes state sequence probabilities
Gets state sequence through backtracking

## Slide 16: Viterbi example
# | Berechnung | Coin 1 (M1) | Coin 2 (M2)
1: Initialisation, O = Tail | δ1(i) = πi * bi(Tail) ψ1(i) = 0 | δ1(M1) = 0,22 ψ1(M1) = 0 | δ1(M2) = 0,12 ψ1(M2) = 0
2 O = Head |  | i = M1: 0,0693 i = M2: 0,0216 δ2(M1) = 0,0693 ψ2(M1) = M1 | i = M1: 0,0528 i = M2: 0,0576 δ2(M2) = 0,0576 ψ2(M2) = M2
3 O = Head |  | i = M1: 0,0218295 i = M2: 0,010368 δ3(M1) = 0,0218295 ψ3(M1) = M1 | i = M1: 0,016632 i = M2: 0,027648 δ3(M2) = 0,027648 ψ3(M2) = M2
4: Termination |  | P* = 0,027648 | 
# | Berechnung | Coin 1 (M1) | Coin 2 (M2)
1: Initialisation, O = Tail | δ1(i) = πi * bi(Tail) ψ1(i) = 0 | δ1(M1) = 0,22 ψ1(M1) = 0 | δ1(M2) = 0,12 ψ1(M2) = 0
2 O = Head |  | i = M1: 0,0693 i = M2: 0,0216 δ2(M1) = 0,0693 ψ2(M1) = M1 | i = M1: 0,0528 i = M2: 0,0576 δ2(M2) = 0,0576 ψ2(M2) = M2
3 O = Head |  | i = M1: 0,0218295 i = M2: 0,010368 δ3(M1) = 0,0218295 ψ3(M1) = M1 | i = M1: 0,016632 i = M2: 0,027648 δ3(M2) = 0,027648 ψ3(M2) = M2
4: Termination |  |  | 
Result: M2  M2  M2 (2,7648 %)

## Slide 18: Modeling
States
  Stops
  Routes
  Neutral
Observations
  GPS coordinates
Problem: GPS coordinates are continuous!
Solution: Probability density function

## Slide 19: Probability density function
Honkela (2001)

## Slide 20: Modeling
States
  Stops
  Routes
  Neutral
Observations
  GPS coordinates
  Time dependent

## Slide 21: State transition probability
To From | Route | Stop | Neutral
Route |  |  | 0
Stop |  |  | 
Neutral | 0 |  | 
To From | Route | Stop | Neutral
Route |  |  | 0
Stop |  |  | 
Neutral | 0 |  | 

## Slide 22: Implementation
Static Route Data: GTFS
Onebusaway

## Slide 25: Evaluation
Trip Id | Route | Number of Observations
8 | 1070T | 137
11 | 1073 | 250
16 | 1004 | 138
17 | 1024 | 472
21 | 2315 | 333
23 | 4741 | 472
26 | 5530 | 281
36 | 1070T | 310
50 | 2150A | 263
51 | 2270 | 89
52 | 2550 | 247

## Slide 26
# | Time | State
1 | 07:51:43 | Neutral
2 | 07:51:49 | Stop 1381121_Malmin tori
5 | 07:52:06 | Route 1077A_77A
7 | 07:52:17 | Stop 1382126_Malmin asema tulo
14 | 07:52:57 | Neutral
15 | 07:53:03 | Stop 1381101_Malmin asema(term.)
18 | 07:53:19 | Route 4519_519
21 | 07:53:35 | Stop 1382123_Ala-Malmi
22 | 07:53:41 | Route 2554_554
23 | 07:53:46 | Stop 1382124_Ala-Malmi
30 | 07:54:23 | Route 2554_554
36 | 07:54:56 | Stop 1382116_Riihenkulma
43 | 07:55:35 | Route 2554_554
50 | 07:56:15 | Route 2554_554
1 | 07:56:20 | Neutral
2 | 07:56:25 | Stop 1382128_Latokartanontie
3 | 07:56:31 | Stop 1382128_Latokartanontie

## Slide 27: The problems
Higher propability for stops
Prioristation of shorter routes
Very low overall probability

## Slide 28: Transition probabilites
To From | Route | Stop | Neutral
Route | 1 if same route 0 else | 1 if stops 0 else | 0
Stop | 1 if stops 0 else | 1 if same stop 0 else | 1
Neutral | 0 | 1 | 0,9

## Slide 29: Observation probabilities
Neutral | Haltestelle | Linie
0.1 | 1.01 | 1

## Slide 30: Results
21 trips tested
  9 correct
  6 partially
  5 wrong

## Slide 33: Conclusion
HMM can be used for SLD
Not better than Live+Gov…
…but more potential
Abused model

## Slide 34: Future Works
Use Trips as states
State transition probabilities relative to time
Test in other cities
Test with further transportation means
Integration in other systems

## Slide 35: Sources
L. R. Rabiner, "A tutorial on hidden Markov models and selected applications in speech recognition," Proceedings of the IEEE, vol. 77, no. 2, pp. 257-286, 2 1989.
R. C. Shah, C.-y. Wan, H. Lu und L. Nachman, „Classifying the Mode of Transportation on Mobile Phones using GIS Information,“ in Proceedings of the 2014 ACM International Joint Conference on Pervasive and Ubiquitous Computing, Seattle, Washington, 2014.
L. Stenneth, O. Wolfson, P. S. Yu und B. Xu, „Transportation Mode Detection using Mobile Phones and GIS Information,“ in Proceedings of the 19th ACM SIGSPATIAL International Conference on Advances in Geographic Information Systems, Chicago, Illinois, 2011.
P. Zhou, Y. Zheng und M. Li, „How Long to Wait? Predicting Bus Arrival Time With Mobile Phone Based Participatory Sensing,“ IEEE Transactions on Mobile Computing, Bd. 13, Nr. 6, pp. 1228-1241, 2014.
A. Honkela, Nonlinear Switching State-Space Models, 2001..

## Slide 36: Sources
Live+Gov: http://liveandgov.eu
Mattersoft: http://www.mattersoft.fi/
HSL: https://www.hsl.fi/

## Slide 37: Questions?